## Slide 1: Systems & Software Security COMSM0050 2020/2021

## Slide 2: Spectre & Meltdown

## Slide 3: Spectre & Meltdown
Late 2017/early 2018
Lots of discussion
Can be fixed in the OS
Spectre category of Attack
Meltdown one instance
  Speculative execution has proven problematic

## Slide 4: Spectre & Meltdown
Late 2017/early 2018
Lots of discussion
Can be fixed in the OS
Computer get slower 
Spectre category of Attack
Meltdown one instance
  Speculative execution has proven problematic

## Slide 5: Spectre & Meltdown
Category of attack affect:
  all OSes
  All hardware (at different degree)
Hardware cannot be patched

## Slide 6: Spectre & Meltdown
Category of attack affect:
  all OSes
  All hardware (at different degree)
Hardware cannot be patched
Can be exploited via simple javascript

## Slide 7: The problem?
Speculative execution
  Try to guess what will be executed
  If correct all good!
  If wrong roll back!

## Slide 8: The problem?
Speculative execution
  Try to guess what will be executed
  If correct all good!
  If wrong roll back!
CPU registers are rolled back…
… but not (always) the CPU cache

## Slide 9: The problem?
Speculative execution
  Try to guess what will be executed
  If correct all good!
  If wrong roll back!
CPU registers are rolled back…
… but not (always) the CPU cache
… and authorization is checked at the end of the pipeline

## Slide 10: The problem?
Speculative execution
  Try to guess what will be executed
  If correct all good!
  If wrong roll back!
CPU registers are rolled back…
… but not (always) the CPU cache
… and authorization is checked at the end of the pipeline
Attacker can get memory value he should not access in the CPU cache

## Slide 11: Meltdown phases
Reading secret: inaccessible memory content chosen by an attacker is loaded into a register
Transmit secret: instruction access cache line based on the secret value
Receive secret: attacker use fetch and reload to determine the accessed cache line
Repeat to dump entire kernel memory

## Slide 12: Meltdown example
if (spec_cond) {
unsigned char value = *(unsigned char *)ptr;
unsigned long index2 = (((value>>bit)&1)*0x100)+0x200; maccess(&data[index2]);
}

## Slide 13: Meltdown example
if (spec_cond) {
unsigned char value = *(unsigned char *)ptr;
unsigned long index2 = (((value>>bit)&1)*0x100)+0x200; maccess(&data[index2]);
}
Under attacker control, we want this branch to be speculatively executed

## Slide 14: Meltdown example
if (spec_cond) {
unsigned char value = *(unsigned char *)ptr;
unsigned long index2 = (((value>>bit)&1)*0x100)+0x200; maccess(&data[index2]);
}
data under attacker control

## Slide 15: Meltdown example
if (spec_cond) {
unsigned char value = *(unsigned char *)ptr;
unsigned long index2 = (((value>>bit)&1)*0x100)+0x200; maccess(&data[index2]);
}
ptr address we don’t have access to

## Slide 16: Meltdown example
if (spec_cond) {
unsigned char value = *(unsigned char *)ptr;
unsigned long index2 = (((value>>bit)&1)*0x100)+0x200; maccess(&data[index2]);
}
bit shift to access a bit of data

## Slide 17: Meltdown example
if (spec_cond) {
unsigned char value = *(unsigned char *)ptr;
unsigned long index2 = (((value>>bit)&1)*0x100)+0x200; maccess(&data[index2]);
}
generate address from data value

## Slide 18: Meltdown example
if (spec_cond) {
unsigned char value = *(unsigned char *)ptr;
unsigned long index2 = (((value>>bit)&1)*0x100)+0x200; maccess(&data[index2]);
}
use address to pull in cache we control

## Slide 19: Meltdown example
char value = *secret_kernel_pointer
mask bit you want to read
calculate offset in data
addres | 
0x100 | 
0x200 | 
0x300 | 

## Slide 20: Meltdown example
char value = *secret_kernel_pointer
mask bit you want to read
calculate offset in data
addres | 
0x100 | 
0x200 | 
0x300 | DATA
IF 1

## Slide 21: Meltdown example
time = rdtsc();
maccess(&data[0x300]);
delta3 = rdtsc() - time;
time = rdtsc();
maccess(&data[0x200]);
delta2 = rdtsc() - time;
access time will depend if value
in cache or not.
Cache side channel.